## Slide 1: 云计算技术
陈果 副教授
湖南大学-信息科学与工程学院-计算机与科学系
邮箱：guochen@hnu.edu.cn
个人主页：1989chenguo.github.io

## Slide 2: What we have learned
What is cloud computing
Cloud Networking
  Physical Structure
  Applications and network traffic
    Quick overview of various typical cloud applications and their architecture
    Measurement and visualization of network traffic
    Implications for networking
  Host networking virtualization
    How host networking is virtualized
    Performance problem of traditional CPU-based method
    Two directions to improve
      SR-IOV
      Open vSwtich

## Slide 3: Addressing & Routing
Ankit Singla
ETH Zürich
P. Brighten Godfrey
UIUC
Some materials from UIUC MOOC
Credits to
Part I: Cloud networking

## Slide 4: Some background
From James F. Kurose and Keith W. Ross

## Slide 5: Network layer concepts

## Slide 6: MAC addresses and ARP
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
MAC (or LAN or physical or Ethernet) address:
  function: used ‘locally” to get frame from one interface to another physically-connected interface (same network, in IP-addressing sense)
  48 bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
  e.g.: 1A-2F-BB-76-09-AD
hexadecimal (base 16) notation
(each “number” represents 4 bits)

## Slide 7: LAN addresses and ARP
each adapter on LAN has unique LAN address
adapter
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)

## Slide 8: LAN addresses (more)
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
analogy:
  MAC address: like Social Security Number
  IP address: like postal address
MAC flat address ➜ portability
  can move LAN card from one LAN to another
IP hierarchical address not portable
  address depends on IP subnet to which node is attached

## Slide 9: ARP: address resolution protocol
ARP table: each IP node (host, router) on LAN has table
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88

## Slide 10: ARP protocol: same LAN
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  dest MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 11: Addressing: routing to another LAN
walkthrough: send datagram from A to B via R
  focus on addressing – at IP (datagram) and MAC layer (frame)
  assume A knows B’s IP address
  assume A knows IP address of first hop router, R (how?)
  assume A knows R’s MAC address (how?)
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B

## Slide 12: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame with R's MAC address as dest, frame contains A-to-B IP datagram
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B

## Slide 13: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
frame sent from A to R
IP
Eth
Phy
frame received at R, datagram removed, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222

## Slide 14: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 15: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 16: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy

## Slide 17: Switch: multiple simultaneous transmissions
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6

## Slide 18: Switch forwarding table
Q: how does switch know A’ reachable via interface 4, B’ reachable via interface 5?
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?

## Slide 19: Switch: self-learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60

## Slide 20: Switch: frame filtering/forwarding
when frame received at switch:
  1. record incoming link, MAC address of sending host
  2. index switch table using MAC destination address
  3. if entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving
  interface */

## Slide 21: Self-learning, forwarding: example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
frame destination, A’, locaton unknown:
flood
A’ A
destination A location known:
A’
4
60
selectively send
on just one link

## Slide 22: Interconnecting switches
switches can be connected together
Q: sending from A to G - how does S1 know to forward frame destined to F via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 23: Institutional network
to external
network
router
IP subnet
mail server
web server

## Slide 24: Two key network-layer functions
forwarding: move packets from router’s input to appropriate router output
routing: determine route taken by packets from source to dest.
  routing algorithms
analogy:
routing: process of planning trip from source to dest
forwarding: process of getting through single interchange

## Slide 25: Now let’s begin!

## Slide 26: Goal: find paths through the network
Server-rack
Switch
How do I reach the destination server?
Notes: Routing: finding paths through the network

## Slide 27: Plug-and-play at Layer 2
Server-rack
Switch
Send to a.b.c.d!
(ARP) a.b.c.d = A::B::C::D::E::F
Notes: Routing: finding paths through the network

## Slide 28: Loop-freedom in forwarding
Notes: Loop prevention is essential!

## Slide 29
I think that I shall never see
A graph more lovely than a tree.
A tree whose crucial property
Is loop-free connectivity.
[Excerpt from “Algorhyme” by Radia Perlman]
Radia Perlman: Inventor of STP
Notes: Invented by Radia Perlman in 1980s
Public domain image: https://commons.wikimedia.org/wiki/File:Radia_Perlman_2009.jpg

## Slide 30: Spanning tree
Disable all other links!
Notes: Traditional approach: spanning tree protocol
core idea: create a tree (animate)
(other links = brought up on failure)
Before criticism: it was a VERY important development!!
plug and play; works over Ethernet, simple
Also: still being used!

## Slide 31: STP works for tree-like networks
Notes: STP works for tree-like networks
Take this example

## Slide 32: STP works for tree-like networks
Notes: essentially, tree + redundancy
BUT expensive to scale (as we’ve discussed earlier)
root switches are made bigger for the cross-traffic, etc.

## Slide 33: STP works for tree-like networks
But  :
loose network capacity
Sensitive to failure
Notes: As we saw in … topology etc. etc.
Networks are scaling horizontally
STP is a bad fit here
  many links left unused
  can’t do multi-pathing (TE, fault tolerance in cloud)
  extremely fragile: partitions, broadcast storms
  traffic volume through root
  slow convergence, seconds!

## Slide 34
Image adapted from “Buchstabensuppe” by Till Westermayer
M-LAG
TRILL
QFabric
SPB
VCS
FabricPath
Notes: An alphabet soup of proposed fixes:
- Hard to assess which (if any!) is “winning”
- Proprietary flavors of standards only add to confusion!
- e.g. TRILL ——> Brocade’s VCS and Cisco’s FabricPath
Debate among operators (e.g. at Nanog)
(https://www.nanog.org/meetings/nanog50/presentations/Monday/NANOG50.Talk63.NANOG50_TRILL-SPB-Debate-Roisman.pdf)
Image: create commons: https://commons.wikimedia.org/wiki/File:Buchstabensuppe.jpg

## Slide 35: Transparent Interconnection of Lots of Links
Link-state protocol between switches
Notes: Let’s (briefly) look at TRILL
Not that it’s the best (still being argued) — just to illustrate one possibility
Link-state protocol between switches (or as trill calls them RBridges)
Learn which hosts are where either from data packets OR announcements OR a directory

## Slide 36: TRILL
All links usable!
Notes: All links are usable
Multi-path routing is available

## Slide 37: TRILL
But  :
Scalability
  Data-center-scale link-state incurs too much overhead
  Data-center-scale flat addressing and routing
  Tricky to handle ARP flood
Need hardware change
Notes: Host sends packet to ingress RBridge
RBridge encapsulates it for transit through to destination RBridge
Nevertheless:
relies on flooding of information
  ~ADDRESS LEARNING
   From Locally Received Native Frames; From Decapsulated Native Frames
   Via Optional End Station Address Distribution Information protocol
   Via Layer-2 Registration protocol(s)
   By manual configuration
single failure domain
requires new equipment that supports it
still concerns about relative “newness” / maturity —> operators are conservative!!

## Slide 38
Scale
Scale
Scale
Scale
Scale
Scale
Scale
Notes: What’s the problem specifically?
- Unmanageable ARP traffic!
- Routing table size

## Slide 39: Traditional solution: subnets
10.2.4.*
10.2.3.*
10.2.*
Notes: How would you solve this problem?! You can break the network down into subnets:
subnets scale routing tables by aggregation

## Slide 40: Traditional solution: VLANs
10.2.4.*
10.2.3.*
10.2.*
Notes: You can break the network down into VLANs
VLANs restrict ARP traffic
What problems does that cause?!!
migrating VM breaks aggregation OR requires change of IP address
management of subnets — size them appropriately, configuration, etc.
Limited size of VLANs because of ARP problems
resource fragmentation; how to use different resources in different subnets and VLANs together? Quickly becomes a management nightmare.

## Slide 41: VL2: “Virtual Layer 2”
VL2 @ Microsoft, ACM SIGCOMM’09
Greenburg, Hamilton, Jain, Kandula, Kim, Lahiri, Maltz, Patel, Sengupta

## Slide 42: VL2: “Virtual Layer 2”
VL2 @ Microsoft, ACM SIGCOMM’09
Greenburg, Hamilton, Jain, Kandula, Kim, Lahiri, Maltz, Patel, Sengupta
Clos network
Name ≠ Location
Randomized load balancing
Notes: We’ll only talk about the name translation part here, leaving load balancing for later. Quiz question: why did VL2 use its own load balancing instead of ECMP?! Note: the motivating factors might have disappeared over time.

## Slide 43: VL2: Location vs. App addresses
VL2 @ Microsoft, ACM SIGCOMM’09
Greenburg, Hamilton, Jain, Kandula, Kim, Lahiri, Maltz, Patel, Sengupta
Virtual IP
Physical IP
Virtual IP: Name
  Unique
Physical IP: Location
  Routing friendly
Notes: Capture packets at host agent, encap with dest. host ToR
Requires this modification at the end-host

## Slide 44: VL2: Address translation
VL2 @ Microsoft, ACM SIGCOMM’09
Greenburg, Hamilton, Jain, Kandula, Kim, Lahiri, Maltz, Patel, Sengupta
Notes: Address translation infra
  agents at hosts for capturing ARPs
  read optimized dir servers
  write opt RSMs
  query multiple directory servers for quick response
  how stale caches at hosts are corrected? Reactively. Packets arrive at the wrong ToR, which communicates with dir servers, which send a correction to the source …

## Slide 45: VL2: Location vs. App addresses
VL2 @ Microsoft, ACM SIGCOMM’09
Greenburg, Hamilton, Jain, Kandula, Kim, Lahiri, Maltz, Patel, Sengupta
Notes: Capture packets at host agent, encap with dest. host ToR
Requires this modification at the end-host

## Slide 46: Routing algorithm classification
Q: global or decentralized information?
global:
all routers have complete topology, link cost info
“link state” algorithms
decentralized:
router knows physically-connected neighbors, link costs to neighbors
iterative process of computation, exchange of info with neighbors
“distance vector” algorithms

## Slide 47: OSPF over IP
I know the
entire topology!
Notes: OSPF is a very mature routing technology
OSPF over IP conveniently sidesteps many STP problems
Simple implementation: link state protocol all-over network
Link-state scalability and single-failure domain issues persist
[Although route summarization and stub-areas help]
TE limited to meddling with link costs
Another option: L2 areas connected over OSPF —> higher complexity

## Slide 48: Link-state Routing
Still encounter scalability issue for super-large cloud

## Slide 49: BGP: Border Gateway Protocol
AS1
AS2
AS3
AS4
AS5
23.18.98.*
Notes: Another design option: BGP … yes. And not I-BGP!
Let’s review (skipping many details relevant to BGP on Internet) …
(Do the review)

## Slide 50: Distance-vector Routing
More scalable and flexible!

## Slide 51: BGP: Border Gateway Protocol
AS1
AS2
AS3
AS4
AS5
23.18.98.* | AS1
23.18.98.*
23.18.98.* | AS5 AS1
23.18.98.* | AS5 AS1
23.18.98.* | AS1
I already know a shorter path!
23.18.98.* | AS2 AS1
23.18.98.* | AS2 AS1
Notes: Another design option: BGP … yes. And not I-BGP!
Let’s review (skipping many details relevant to BGP on Internet) …
(Do the review)

## Slide 52: BGP in the data center
AS 64999
AS 64981
AS 65111
AS 65000
AS 65001
AS 65002
AS 65003
Divide groups of switches and servers into Ases;
Use BGP!
Notes: Facebook has mentioned using BGP, doesn’t use server virtualization
IP aggregation makes routing tables small
No more L2 scalability concerns (no message flooding)
BGP is well-tested
multi-path w ECMP (more details later)
vs OSFP:
Easier debugging (AS_PATH is visible)
Inter-operability across vendors is greater than OSPF
Every link failure in OSPF => flood. Not here.
Per-hop traffic engineering (can announce arbitrary subset of routes)
Cons:
VM migration is more complex
slow convergence (although route changes are infrequent)
complexity? (auto-gen of configs)
Route manipulations may also be done via central coordination (SDN)!!

## Slide 53: Routing
Notes: So far: routing, i.e., figuring out a set of paths
Now, how to use these paths?
Besides connectivity, we want
fault tolerance
efficient traffic engineering
These are things multipath routing helps with …

## Slide 54: Multipath routing
Notes: The example we’ll work with …
The fat-tree topology
has lots of parallel paths
can we exploit them for fault tolerance and TE?
TE goal: want to minimize congestion
Difficult problem!
  traffic is dynamic
  computationally expensive even when centralized
  distributed algorithm needed
Approximation: randomized spreading of traffic with ECMP
Image: from the fat-tree paper here: http://ccr.sigcomm.org/online/files/p63-alfares.pdf

## Slide 55: Equal cost multi-path (ECMP)
10.2.0.3 | port 1
10.2.0.3 | port 2
Choose uniformly
at random!
Notes: Let’s see how ECMP works.
To send traffic from one of these nodes to the other …
forward packet to switch
now, two choices (known from routing protocol) (animate)
routing table entries might look something like this (animate)
pick one uniformly at random!

## Slide 56: Equal cost multi-path (ECMP)
Choose uniformly
at random!
10.2.0.3 | port 1
10.2.0.3 | port 2
Notes: BUT … packet spraying is problematic for TCP

## Slide 57: Equal cost multi-path (ECMP)
Output port = hash (packet header)
1
2
Notes: (Walk through example)
Explain solution: flow-level hashing

## Slide 58: Equal cost multi-path (ECMP)
Notes: ECMP can be done independently at each hop!
Number of paths increases multiplicatively
So 2 X 2 = 4 path choices here

## Slide 59: Equal cost multi-path (ECMP)
Notes: ECMP is simple
Works over both L2 and L3 routing
Works quite well for large number of small flows
The use of a random hashing to map flows to outgoing ports works particularly well if most flows are short.
Sophisticated operators (e.g. Facebook):
controller monitors imbalances, fixes paths if necessary
Source of information FB talk (https://youtu.be/kcI3fGEait0?t=1033)

## Slide 60: ECMP: local, oblivious choices
Cannot avoid distant failures!
x
IEEE/ACM Transactions on Networking, 2017
Notes: A more serious issue, perhaps, is that ECMP only makes local decisions, without knowledge of failures further on a path. If some later link is down, ECMP, making only these local choices can do nothing to avoid it. (Note how in this topology, there is another failure-free path available, while from the node which first sees the failure on this path, there are no paths.)

## Slide 61: ECMP: traffic imbalance
Output port = hash (packet header)
Notes: But the randomization will sometimes lead to imbalance in flow assignments. This can cause long-lasting congestion if multiple long-lasting data flows are mapped onto the same links. As we noted earlier, we can’t do randomization at packet level, because that causes packet re-ordering. However, we don’t necessarily have to do it at flow-level either. This is where the idea of a “flowlet” is useful.

## Slide 62: Flowlets
Flowlets
>𝝙l
>𝝙l
ACM SIGCOMM, 2007
Notes: If the gap between groups of packets is larger than a conservative estimate of the latency difference between the paths, we can send them on different paths without risk of reordering.
Such packet groups are called flowlets.
This helps make load balancing more fine-grained, and unlikely to run into long-term congestion problems caused by random choices.
This idea was proposed by Kandula et al. in 2007.

## Slide 63: CONGA: edge based monitoring
ACM SIGCOMM, 2014
Notes: Recent work proposes a solution to this problem: the key idea is to monitor congestion on paths in real-time, and pick the least congested path (on a flowlet granularity)

## Slide 64: Design: Leaf-to-Leaf Feedback
H9
H1
H2
H3
H4
H5
H6
H7
L1
H8
1
2
3
0
Track path-wise congestion metrics (3 bits) between each pair of leaf switches
Congestion-To-Leaf
Table @L0
Dest Leaf
Path
0
1
2
L1
L2
3
Congestion-From-Leaf
Table @L2
Src Leaf
Path
0
1
2
L0
L1
3
L0L2
Path=2
CE=5
5
5
L0
L2
L0L2
Path=2
CE=0
L0L2
Path=2
CE=5
L0L2
Path=2
CE=0
L2L0
FB-Path=2
FB-Metric=5
5
1
1
4
3
7
2
Rate Measurement Module
measures link utilization
pkt.CE  max(pkt.CE, link.util)

## Slide 65: Design: LB Decisions
Send each packet on least congested path
H1
H2
H3
H4
H5
H6
H7
L0
L1
L2
H9
H8
Congestion-To-Leaf
Table @L0
Dest Leaf
Path
0
1
2
L1
L2
3
5
5
1
1
4
3
7
2
1
2
3
0
L0  L1: p* = 3
L0  L2: p* = 0 or 1
flowlet [Kandula et al 2007]

## Slide 66: Multi-path Transport
ACM SIGCOMM, 2011
USENIX NSDI, 2011

## Slide 67
Receiver
Sender
SF1
SF2
SF3
SF1
SF2
SF3
CWND2
CWNDtotal
CWND1
CWND3
Multi-path
Congestion Control
Data Distribution
Sub-flows: Implicitly mapping to physical paths
Remain ECMP unchanged!
Multipath TCP
Notes: Before introducing the detailed design of FUSO, I’d like to give some background on multi-path transport.
In multipath transport, a TCP flow is divided into multiple sub-flows.

## Slide 68: Multi-path Transport for Hardware-based Network Stack
USENIX NSDI, 2018

## Slide 69: Other possibilities?
Great freedom and resources!
Notes: single-entity control
large switch forwarding tables (tens of thousands of L2, L3 entries)
topology is known, controlled by the operator
topologies have lots of links and paths
So watch out for more developments in this space.

## Slide 70: Reading materials for group projects
“VL2: A Scalable and Flexible Data Center Network”, SIGOMM 2009
“F2Tree: Rapid Failure Recovery for Routing in Production Data Center Networks”, TON 2017
“CONGA: Distributed Congestion-Aware Load Balancing for Datacenters”, SIGCOMM 2014
“Resilient Datacenter Load Balancing in the Wild”, SIGCOMM 2017
“Let It Flow: Resilient Asymmetric Load Balancing with Flowlet Switching”, NSDI 2017
“Improving Datacenter Performance and Robustness with Multipath TCP”, SIGCOMM 2011
“Design, implementation and evaluation of congestion control for multipath TCP”, NSDI 2011
“Multi-Path Transport for RDMA in Datacenters”, NSDI 2018

## Slide 71: Thanks!
陈果 副教授
湖南大学-信息科学与工程学院-计算机与科学系
邮箱：guochen@hnu.edu.cn
个人主页：1989chenguo.github.io